## Slide 1: PHYSARUM INSPIRED BICYCLE LANE NETWORK DESIGN IN CONGESTED MEGA CITY
2
+
Supervisor:
Dr. Md. Aminul Haque Akhand
Professor
Presentator:
Md. Ahsan Habib
Roll: 1507082
Department of Computer Science and Engineering
Khulna University of Engineering & Technology

## Slide 2
OUTLINE
Introduction
Conclusion
Related Study
Experimental Study
References
Methodology
Specific Aim
Global Aim
Challenges

## Slide 3
Introduction
A transit network is a spatial network describes a structure which permits either vehicular movement or flow of some commodity.
The Network Design Problem (NDP) is known as one of the most complex and challenging transportation problems for many years.
Effective and efficient transit network can minimize the total travel time, cost, CO2 emission reduction, fuel usage reduction, etc.

## Slide 4
INTro. CONDT..
Physarum Polycephalum, also named as slime mold is:
  Multi-headed
  Brainless
  Giant multi-nucleated
  Single-celled protist
which can solve different complex problems.
Physarum networks are believed to have achieved a good balance between cost, efficiency and resilience.

## Slide 5
Global AIM
The global purpose is to construct efficient transit network in mega city, concerned with:
- Minimization of travel time
- Minimization of cost
- Minimization of CO2 emission reduction
- Efficient & effective network design
- Eco-friendly environment

## Slide 6
Authors | Year | Title of Paper | Journal | Contribution
Tero et al. | 2010 | Rules for Biologically Inspired Adaptive Network Design | Science | Tokyo Rail Network construction
Adamatzky et al. | 2011 | Rebuilding Iberian motorways with slime mould | Biosystems | Iberian motorway network construction
Adamatzky et al. | 2011 | Approximating Mexican highways with slime mould | Natural Computing | Mexican Federal highway network construction
Adamatzky et al. | 2013 | Slime mould imitates transport networks in China | International Journal of Intelligent Computing and Cybernetics | Slime mould protoplasmic networks on major urban areas of China
Tsompanas et al. | 2015 | Evolving Transport Networks With Cellular Automata Models Inspired by Slime Mould | IEEE Transactions on Cybernetics | Physarum-inspired cellular automaton (CA)-based network designing model
Zhang et al. | 2016 | A Physarum-inspired approach to supply chain network design | Science China Information Sciences | Supply chain network design
RELATED STUDY

## Slide 7
SPECIFIC AIM
We want to construct bicycle lane network in congested area Motijheel and try to move towards the green city.
For this,
We create a bicycle lane network using modified Physarum-inspired technique.
We consider bicycles to move around of Motijheel.
Finally, we extend it to apply mega city Dhaka using electric bicycle as vehicle.

## Slide 8
Challenges
There exist lots of challenges in any mega city:
- Road conditions are not good enough
- Cycling lanes & footways are hardly available
- Worst traffic
- Fuel shortages
- Huge CO2 gas emission
- Air pollution & noise pollution
- Unhealthy environment

## Slide 9
METHODOLOGY
Flux Update
Conductivity Update
Initial Conductivity
Pressure Update
Edge Eliminate
The bicycle lane network is constructed using the following five steps using modified Physarum inspired technique:

## Slide 10
METHODOLOGY
Flux Update
Conductivity Update
Pressure Update
Edge Eliminate
Initial Conduct-ivity
The initial conductivity is calculated using the following equation.
In the above equation,
    - conductivity of the edge,
    - radius/width of the edge,
- coefficient of viscosity.
First Step:

## Slide 11
METHODOLOGY
Flux Update
Conductivity Update
Pressure Update
Edge Eliminate
Initial Conductivity
The pressures can be determined using the Poisson equation network below by considering the flux conservation law at each vertex.
In the above equation,
- the set of vertices linked to vertex j,
- the amount of flux flowing into and out of the node of the source.
Second Step:

## Slide 12
METHODOLOGY
Flux Update
Conductivity Update
Pressure Update
Edge Eliminate
Initial Conductivity
Specifically, the flux () in edge (i,j) is given by the Hagen-Poiseuille equation below.
In the above equation,
- conductivity of the edge,
- length of the edge,
- pressure of vertices i and j.
Third Step:

## Slide 13
METHODOLOGY
Flux Update
Conductivity Update
Pressure Update
Edge Eliminate
Initial Conductivity
Therefore, the conductivity update formula can explain the change in tubular thickness of Physarum as follows,
here
- an increasing function,
- a positive constant.
Fourth Step:

## Slide 14
METHODOLOGY
Flux Update
Conductivity Update
Pressure Update
Edge Eliminate
Initial Conductivity
In Edge elimination step, edges with conductivity lower than the threshold value are cut off from the network.
Third-step to fifth-step is repeated in finite iterations.
Fifth Step:

## Slide 15
EXPERIMENTAL STUDY
Figure 1. Motijheel area
Figure 2. Existing network of Motijheel area
For Motijheel Area

## Slide 16
EXPERIMENTAL STUDY
(A) t = 10
Figure 3. Network growing steps of Motijheel area.
(A) t = 50
(A) t = 20
Motijheel Area contd.

## Slide 17
EXPERIMENTAL STUDY
Figure 4. Final network of Motijheel area.
Motijheel Area contd.

## Slide 18
EXPERIMENTAL STUDY
Transit | % of Transit Reduction (assumption) | Transit Reduces | Ride Reduce (km) | Fuel (litres) | User cost (tk) | Time saves (mins) | CO2 emission (g)
Bus | 5% | 6370 | 127400 | 25480 | 216580 | 709800 | 1.13 108
Car | 2% | 5865 | 58650 | 2933 | 190613 | 326764 | 1.51 107
Taxicab | 10% | 3660 | 366000 | 14640 | 18300000 | 2039143 | 8.67 107
Motor cycle | 10% | 72480 | 1087200 | 21744 | 1935216 | 6057257 | 4.35 107
Total fuel, user cost, time & CO2 emission reduces |  |  |  | 64797 | 20642409 | 9132964 | 2.58 108
Transit | % of Transit Reduction (assumption) | Transit Reduces | Ride Reduce (km) | Fuel (litres) | User cost (tk) | Time saves (mins) | CO2 emission (g)
Bus | 5% | 6370 | 127400 | 25480 | 216580 | 709800 | 
Car | 2% | 5865 | 58650 | 2933 | 190613 | 326764 | 
Taxicab | 10% | 3660 | 366000 | 14640 | 18300000 | 2039143 | 
Motor cycle | 10% | 72480 | 1087200 | 21744 | 1935216 | 6057257 | 
Total fuel, user cost, time & CO2 emission reduces |  |  |  | 64797 | 20642409 | 9132964 | 
Fuel saving = 64.8 thousand litres
User cost saving = 20.64 million tk
Time saving = 0.15 million working hours
CO2 emission reduces = 0.26 million kg
Impact - Motijheel Area

## Slide 19
EXPERIMENTAL STUDY
Figure 5. Dhaka city Map
Figure 5. Constructed network of Dhaka city
Entire Dhaka City

## Slide 20
EXPERIMENTAL STUDY
Transit | % of Transit Reduction (assumption) | Transit Reduces | Ride Reduce (km) | Fuel (litres) | User cost (tk) | Time saves (mins) | CO2 emission (g)
Bus | 10% | 12740 | 254796 | 50959 | 1.27 million | 7.2 × 107 | 2.3 108
Car | 5% | 14663 | 146630 | 7331 | .45 million | 1.04 106 | 3.8 107
Taxicab | 20% | 7320 | 732000 | 29280 | 36.5 million | 5.2 106 | 1.7 108
Motor cycle | 50% | 362400 | 5436000 | 108720 | 8.5 million | 3.8 107 | 2.2 108
Total fuel, user cost, time & CO2 emission reduces |  |  |  | 195570 | 46.72 million | 1.16 108 | 6.58 108
Transit | % of Transit Reduction (assumption) | Transit Reduces | Ride Reduce (km) | Fuel (litres) | User cost (tk) | Time saves (mins) | CO2 emission (g)
Bus | 10% | 12740 | 254796 | 50959 | 1.27 million | 7.2 × 107 | 
Car | 5% | 14663 | 146630 | 7331 | .45 million |  | 
Taxicab | 20% | 7320 | 732000 | 29280 | 36.5 million |  | 
Motor cycle | 50% | 362400 | 5436000 | 108720 | 8.5 million |  | 
Total fuel, user cost, time & CO2 emission reduces |  |  |  | 195570 | 46.72 million |  | 
Fuel saving = 0.2 million litres
User cost saving = 46.72 million tk
Time saving = 1.9 million working hours
CO2 emission reduces = 0.66 million kg
Impact - Enitre Dhaka

## Slide 21
CONCLUSION
In unorganized and unplanned mega city, we have developed an bicycle network.
With that, most problems like traffic jams, environmental pollution, fuel shortages will be reduced.
The costs will be reduced and people can have some physical activity also.
This also enriches the economy and the environment.

## Slide 22
REFERENCES
https://en.wikipedia.org/wiki/Sustainable_city
http://archive.boston.com/business/blogs/global-business-hub/2013/10/12_essential_as.html
Tero et al., “Rules for Biologically Inspired Adaptive Network Design,” Science (80-. )., vol. 327, no. 5964, pp. 439–442, Jan. 2010.
A. Adamatzky and R. Alonso-Sanz, “Rebuilding Iberian motorways with slime mould,” Biosystems, vol. 105, no. 1, pp. 89–100, Jul. 2011.
A. Adamatzky, G. J. Martínez, S. V. Chapa-Vergara, R. Asomoza-Palacio, and C. R. Stephens, “Approximating Mexican highways with slime mould,” Nat. Comput., 2011.
A. Adamatzky, X.-S. Yang, and Y.-X. Zhao, “Slime mould imitates transport networks in China,” Int. J. Intell. Comput. Cybern., vol. 6, no. 3, pp. 232–251, Aug. 2013.
M. Becker, “Design of fault tolerant networks with agent-based simulation of Physarum polycephalum,” in 2011 IEEE Congress of Evolutionary Computation (CEC), 2011, pp. 285–291.
M.-A. I. Tsompanas, G. C. Sirakoulis, and A. I. Adamatzky, “Evolving Transport Networks With Cellular Automata Models Inspired by Slime Mould,” IEEE Trans. Cybern., vol. 45, no. 9, pp. 1887–1899, Sep. 2015.
X. Zhang, A. Adamatzky, X.-S. Yang, H. Yang, S. Mahadevan, and Y. Deng, “A Physarum-inspired approach to supply chain network design,” Sci. China Inf. Sci., vol. 59, no. 5, p. 052203, May 2016.

## Slide 23
Thank You..

## Slide 24
Details Calculation
Assumption: Car - 5%, Motor cycle - 50%, Bus - 10%, Taxicab - 20% reduces.
  Time saving bus = 254796 × 40 × ( 8.57 – 1.5) mins
  Time saving car = 146634 × (8.57 – 1.5) mins
  Time saving taxicab = 732000 × (8.57 – 1.5) mins
  Time saving motor cycle = 5.4 × 106 × (8.57 – 1.5) mins
  Fuel saving for bus = 254796 km × 1/5 litres
  Fuel saving for car = 146634 km × 1/20 litres
  Fuel saving for taxicab = 732000 km × 1/25 litres
  Fuel saving for motor cycle = 5.4 × 106 km × 1/50 litres
  CO2 reduction for bus = .1×127398×20×887 gm
  CO2 reduction for car = .05×293268×10×258 gm
  CO2 reduction for taxicab = .2×36600×100×237 gm
  CO2 reduction for motorcycle = 0.5× 724800×15×40 gm
Total working time saving = 1.9 million hours
Total fuel saving = 0.2 million litres
Total CO2 emission reduction = 6.58 × 105 kg

## Slide 25
MOTIVATION
We aim to apply our model in unorganized and unplanned mega city like Dhaka where exits some challenges discussed in followings:
No separate cycling roads
No available spaces in footway exist for bi-cycle riding
Traffic jam
Air Pollution (AQI- 309; Standard- 50)
Noise Pollution (Level 80-110dB; Standard- 60dB)
Scarcity of natural gas and petroleum
Automobiles are increasing around 10% annually